## Slide 1
Project mid presentation
Presented by : Olga Liberman & Yoav Shvartz
Supervisor : Moshe Porian
28.1.2012
Symbol Generator
Notes: הערות:
מי אנחנו. תזכורת ...

## Slide 2: Contents
Reminder
Top Architecture
Micro architecture
Schedule
Notes: הצגת תוכן המצגת:
מבט כללי על הפרוייקט ולמה הוא נועד
הארכיטקטורה העליונה ומבט כולל על מבנה המערכת
הסברת עקרון הפעולה של כל בלוק
הלו"ז של הפרוייקט

## Slide 3: Reminder
Generating symbols on display screen using:
  Cyclone II FPGA
  Host communication via UART protocol
  Internal communication via Wishbone protocol
Input - Grayscale symbols 32 x 32 pixels
  saved in external SDRAM
Output - Grayscale image resolution 640x480 pixels
Main clock freq. 133MHz
VESA (monitor) freq. 40 MHz
Notes: תזכורת:
ביצוע שינויים על גבי מסך תוך כדי יצירת התמונה ללא צורך בשמירת פריים שלם.
משתמשים בתשתית של פרוייקט קודם.
התקשורת החיצונית בין המערכת למחשב תבוצע באמצעות פרוטוקול UART
התקשורת בין הבלוקים הפנימיים תבוצע בהתאם לפרוטוקול WISHBONE
כל הבלוקים עובדים בתדר של 133MHz למעט הVesa

## Slide 4
TX Path
Memory
Management
RX Path
SDRAM Controller
WBS
WBS
WBM
WBM
WBS
WBS
Display
Controller
WBS
Host
(Matlab)
VGA
Display
IS42S16400 SDRAM
WBM
WBM
UART
UART
VESA
Wishbone
INTERCON
Reminder
Notes: תזכורת:
הצגה כללית של תשתית הפרוייקט הקודם

## Slide 5
Reminder
20
15
Address of symbol (0,0) in the SDRAM
Address of symbol (14,19) in the SDRAM
RAM
Video Frame
1 | 2 | 3 |  | 16
17 | 18 | 19 |  | 32
1 | 2 | 3 |  | 16
17 | 18 | 19 |  | 32
1 | 2 | 3 |  | 16
17 | 18 | 19 |  | 32
SDRAM
Symbol # i
1
1
1
1
1
FIFO
0/1
Address of the symbol in the SDRAM
X
Y
Op-Code
Notes: תזכורת:
הבלוקים השונים שבהם נשתמש. לחזור בקצרה על הרעיון הכללי
RAM: כל בלוק X,Y במסך מקבל כתובת משלו בRAM כשכתובת זו מכילה את מיקום הביט הראשון בSDRAM של הסמל אותו רוצים להציג בבלוק.
גודל: 300X13 (אורך = 20X15 בלוקים בפריים אחד, רוחב = 11 כמספר הביטים לייצוג שורה ב SDRAM + 2 כמספר הביטים לייצוג 4 Banks של SDRAM .
כל סמל מורכב מ 32 שורות ובכל שורה 32 פיקסלים. כל סמל נשמר ב 2 שורות ב.SDRAM
הסמלים מועברים ל-2 FIFOs שעושים toggeling ביניהם, פעם אחת כותבים לאחד (מ SDRAM) ומעבירים לאחר( ל VESA ) ופעם שניה התפקידים מחלפים.

## Slide 6
TX Path
Memory
Management
RX Path
SDRAM Controller
WBS
WBS
WBM
WBM
WBS
WBS
Display
Controller
WBS
Host
(Matlab)
VGA
Display
IS42S16400 SDRAM
WBM
WBM
UART
UART
VESA
Wishbone
INTERCON
Top Architecture

## Slide 7
Top Architecture
WBS
WBM
Opcode Unite
OPU
RAM
OPU -FIFO
Re-Mng
FIFO A
FIFO B
MUX
Dual Clk FIFO
SDRAM
Memory
Reg
VESA
Controller
- 133 MHz
40 Hz
WBS bus
Data bus
Write
bus
Read
bus
Re Mng Valid
Vsync
WBM bus
Req_in_trg
Write bus
Write bus
Data A
Data B
Data
Data
MUX Sel
VESA Bus
Opcode
Notes: תיאור כללי של המערכת (בירוק- בלוקים שלנו, בורוד – בלוקים של בארי):
מגיע חבילת שינויים מהמשתמש. OPU מאחד את כל 3 מקבצים של 8 סיביות לopcode 1. את השינויים שומרים ב OPU-FIFO .
כש Vsync עולה, OPU-FIFO מעדכן את ה RAM בחבילת השינויים הבאה. כשהסתיים העדכון, Re_Mng_Valid עולה.
Re_Mng מתחיל לנהל את הכתיבה לVESA:
קוראים מה SDRAM את הסמל הרלוונטי תוך שימוש ב Memory Reg ששומר כתובות של ה SDRAM, שליחת נתונים ל FIFO A/B , משם ל DC FIFO, משם ל
VESA Controller וממנו למסך. VESA Controller שולח Req_in_trg כדי ש Re_Mng "יתכונן" לשליחת המידע.

## Slide 8
Micro Architecture - OPU
Goal:
1.Unites every 3 packs of MPD into 1 opcode by a FSM.
2.Sending the changes to OPU - FIFO
idle
MPD1
MPD2
MPD3
* When we reach state MPD3 then we have 1 opcode (24 bit).
* MPD = Message Pack Data
MPD 1
MPD 2
MPD 3
opcode
Notes: MPD= Message Pack Data (1 pack of 8 bits that is transmitted in the Payload field. There can be more than 1 MPD in Payload field and the number of MPD is represented by the field Data Length in the transmitted message.
במצב MPD3 אנחנו מעברים את השינוי ל OPU-FIFO

## Slide 9: Micro Architecture – OPU pins:
Wbs_adr_i [9..0]
Wbs_tga_i [9..0]
Wbs_dat_i [7..0]
Wbs_cyc_i
Wbs_stb_i
Opcode Unite
Wbs_ack_o
Wbs_stall_o
Wbs_err_o
Clk_133
reset
Opcode_fifo_wr_en
Opcode_fifo_data_in[23..0]
Return

## Slide 10
Micro Architecture – OPU FIFO
Goal:
Stores commands from the OPU.
Sending the changes to RAM.
Size : 300 x 24 (rows x bits)
RAM_adr_wr[8..0] = 20*x + y
Com_type = ‘0’ (remove a symbol)  RAM_data_in[0..13]= "0…0"
Com_type = ‘1’(add a symbol)  RAM_data_in [0..13]= "com_add".
0/1
Com add
X
Y
Notes: The Opcode FIFO receives the opcodes from the Opcode Unite block. It stores the opcodes until the VSYNC of the VESA is active. Then, the opcodes will be written to the calculated row in the RAM: RAM_adr_wr[8..0] = 20*x + y.
If com_type = 0 (remove a symbol) then RAM_data_in[0..13]= "0…0"
Else (add a symbol) RAM_data_in [0..13]= "com_add".
* Com_type = the first bit indicating if we want to add or remove the symbol

## Slide 11: Micro Architecture – OPU FIFO pins:
op_fifo_wr_en
op_fifo_data_in[23..0]
Opcode FIFO
300 x 24 (row x bit)
(VSYNC) op_fifo_rd_en
Clk_133
reset
RAM_adr_wr[8..0]
RAM_wr_en
RAM_data_in[13..0]
Op_fifo_empty
Op_fifo_full
Op_fifo_used[8..0]
rd_mng_en
Return

## Slide 12
Micro Architecture - RAM
Goal:
Stores the address of the
symbol in the SDRAM .
Address of symbol (0,0) in the SDRAM
Address of symbol (14,19) in the SDRAM
20
15
1 | 2 | 3 |  | 16
17 | 18 | 19 |  | 32
1 | 2 | 3 |  | 16
17 | 18 | 19 |  | 32
1 | 2 | 3 |  | 16
17 | 18 | 19 |  | 32
SDRAM
RAM
Video Frame
Address of symbol (0,1) in the SDRAM
Notes: In RAM we save the row in SDRAM, in which the symbol of this block starts. (14 bits)

## Slide 13: Micro Architecture – RAM pins:
RAM_adr_wr[8..0]
RAM_wr_en
RAM_data_in[13..0]
RAM
300 x 14 (row x bit)
RAM_adr_rd[8..0]
RAM_rd_en
RAM_data_out[13..0]
RAM_out_valid
Clk_133
reset
Return

## Slide 14
Micro Architecture – Rd_Mng
Goal:
The "brain" of the Symbol Generator block
Functionality:
Calculating relevant row in the RAM and receiving data.
Calculating row and column in the SDRAM (where the symbol sits).
Managing the toggling between the two FIFOs, using FSM.
Notes: פירוט האלגוריתם יעשה בע"פ במידה ונדרש לכך

## Slide 15
Micro Architecture – Rd_Mng
FSM:
IDLE
WRITE A READ B
reset
READ A WRITE B
RAM updated
Rd_mng_en
WRITE A
READ B
Req_in_trg
(req_in_trg)
AND
(NOT last row of the frame)
(req_in_trg)
AND
(last row of the frame)
req_in_trg
Finished deliver last row to
DC FIFO
Notes: פירוט ה Toggeling:
מתחילים ממצב idle.
כשה RAMמסיים להתעדכן בשינויים המוזנים לו ע"י OPU-FIFO , נשלח סיגנל ל Rd_Mng המורה לו להתחיל לפעול ולקרוא מ SDRAM אל FIFO – A.
בכל פעם שה VESA מבקשת מחזור כתיבה אליה (req_in_trg), אנו קוראים מ FIFO אחד וכותבים לאחר.
ה toggling נעשה עד שמגיעים לשורה האחרונה ב VEAS, בה יש לקרוא רק מ FIFO B.

## Slide 16: Micro Architecture – Rd_Mng pins:
RAM_data_out[13..0]
RAM_out_valid
Wbm_dat_i[7..0]
Read_Manager
(=RM)
RAM_rd_en
RAM_adr_rd[8..0]
Wbm_stall_i
Wbm_ack_i
Wbm_err_i
Wbm_add_o[9..0]
Wbm_tga_o[9..0]
Wbm_cyc_o
Wbm_std_o
Clk_133
reset
Receiving data from SDRAM
Wbm_dat_o[7..0]
Requesting data from SDRAM
FIFO_A_rd_en
FIFO_A_data_in[7..0]
FIFO_A_wr_en
FIFO_B_rd_en
FIFO_B_data_in[7..0]
FIFO_B_wr_en
req_in_trg

## Slide 17
Schedule