## Slide 1
Final presentation – part B
Olga Liberman and Yoav Shvartz
Advisor: Moshe Porian
April 2013
Symbol Generator
2 semester project

## Slide 2: Contents
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis – P&R
Summary
Notes: לתאר על מה נעבור במצגת

## Slide 3: Motivation
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
Generating symbols on display screens is an essential operation these days.
Commonly used in varies applications:
Mobile phones
Televisions
Military applications
Notes: משתמשים בהצגת סמלים על מסך בכל מקום

## Slide 4: Goals
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
Building SG block for FPGA in VHDL environment which:
1. receive changes on screen from Host.
2. apply to external memory (SDRAM).
3. dispatch new display onto screen.
Integrating the block into an existing platform.
Creating Graphical User Interface tool for
convenient use.
Notes: לפרט על מטרות הפרוייקט

## Slide 5: Requirements
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
Reused Platform
Transmit 640x480 grayscale frames
Frames divided into 20x15 (row x column) aligned blocks.
Each symbol size is 32X32 pixels
  Required size in SDRAM: (num of symbols) x 32 x 32 bytes
Clk used:
1. 40 MHz VESA
2. 100MHz System
3. 133MHz SDRAM
Notes: דרישות הפרוייקט, בדגש על התבססות על מערכת קיימת

## Slide 6: Video
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
Notes: דרישות הפרוייקט, בדגש על התבססות על מערכת קיימת

## Slide 7: Bird’s eye
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
Symbol Generator
Platform
Storage Devices
Displays
Data
Generators
Notes: איפה אנחנו "חיים" בפלטפורמה

## Slide 8: Platform
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
TX Path
Memory
Management
RX Path
SDRAM Controller
WBS
WBS
WBM
WBM
WBS
WBS
Display
Controller
WBS
VGA
Display
IS42S16400 SDRAM
WBM
WBM
UART
UART
VESA
Wishbone
INTERCON
Notes: איפה אנחנו "חיים" בפלטפורמה

## Slide 9: Symbol Generator
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
WBS
WBM
Opcode Unite
OPU
RAM
Opcode Store
Mng
FIFO A
FIFO B
MUX
Dual Clk FIFO
SDRAM
Addr
Reg
VESA
Controller
- 100 MHz
40 MHz
WBS bus
Data bus
Mng Valid
Vsync
Req_ln_trg
Data
Data
VESA Bus
Opcode
Rd _en A/B
Notes: תזכורת על ה TOP שלנו

## Slide 10: Platform Changes
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
SDRAM Controller
WBS
WBS
WBS
WBS
Wishbone
INTERCON
WBM
RX Path
WBM
TX Path
WBM
WBS
VESA
Ctrl
SG TOP
Display
Controller
DC FIFO
100MHz
40MHz
SG WBM_IF
Memory
Management
TY
Ad
1. Expanding Address Space for supporting more registers
2. Enabling writings from Disp Ctrl to Mem Mng
3. Adding SG WBM IF for WB communication
Notes: הצגת השינויים הכוללים בפלטפורמה

## Slide 11: Display Controller
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
Notes: התמקדות ספציפית ב Display Controller ואיך הוא נראה כיום עם הבלוקים שלנו

## Slide 12: Data Flow
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
Two parts:
1. Initialization:
      SG RAM Initialization
      SDRAM Initialization
2. Continuous use
      Opcodes transmission
      SDRAM read address update
      Symbols extraction
Notes: מסבירים על ה Data flow ומקשרים לשקף הבא...

## Slide 13: UART: Opcode Packets
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
SOF
Type
Address
Data Length
Data (Payload)
CRC
EOF
Symbol Generator register address is 0x10
Length is 0x0383, 899 in decimal
It means 900 bytes in the UART chunk
Type 0x80 means writing to a register
Payload that sets the Symbol Generator RAM with zeros
SOF
Type
Address
Data Length
Data (Payload)
CRC
EOF
Notes: את תהליך זרימת המידע מתחילים בשליחת קבצים שמכילים את פקטות המידע. דוגמא לכך הוא תהליך איתחול הSDRAM בסמלים

## Slide 14: Initialize RAM
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
SDRAM Controller
WBS
WBS
WBS
WBS
WBM
RX Path
WBM
TX Path
WBM
WBS
VESA
Ctrl
SG TOP
Display
Controller
DC FIFO
100MHz
40MHz
SG WBM IF
Memory
Management
TY
Ad
Mem Ctrl wr
Mem Ctrl rd
Arbiter
INTERCON
X
INTERCON
Y
INTERCON
Z

## Slide 15: Initialize SDRAM
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
SDRAM Controller
WBS
WBS
WBS
WBS
WBM
RX Path
WBM
TX Path
WBM
WBS
VESA
Ctrl
SG TOP
Display
Controller
DC FIFO
100MHz
40MHz
SG WBM IF
Memory
Management
TY
Ad
Mem Ctrl wr
Mem Ctrl rd
Arbiter
INTERCON
X
INTERCON
Y
INTERCON
Z

## Slide 16
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
SDRAM Controller
WBS
WBS
WBS
WBS
WBM
RX Path
WBM
TX Path
WBM
WBS
VESA
Ctrl
SG TOP
Display
Controller
DC FIFO
100MHz
40MHz
SG WBM IF
Memory
Management
TY
Ad
Mem Ctrl wr
Mem Ctrl rd
Arbiter
INTERCON
X
INTERCON
Y
INTERCON
Z
Opcodes Transmission

## Slide 17: SDRAM Read Address Update
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
SDRAM Controller
WBS
WBS
WBS
WBS
WBM
RX Path
WBM
TX Path
WBM
WBS
VESA
Ctrl
SG TOP
Display
Controller
DC FIFO
100MHz
40MHz
SG WBM IF
Memory
Management
TY
Ad
Mem Ctrl wr
Mem Ctrl rd
Arbiter
INTERCON
X
INTERCON
Y
INTERCON
Z

## Slide 18: Symbols Extraction
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
SDRAM Controller
WBS
WBS
WBS
WBS
WBM
RX Path
WBM
TX Path
WBM
WBS
VESA
Ctrl
SG TOP
Display
Controller
DC FIFO
100MHz
40MHz
SG WBM IF
Memory
Management
TY
Ad
Mem Ctrl wr
Mem Ctrl rd
Arbiter
INTERCON
X
INTERCON
Y
INTERCON
Z

## Slide 19: Test plan
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
Data scenarios - Different data amounts
1. Adding / removing several symbols to a frame.
2. Adding the same symbol in different locations in a frame.
3. Checking the “Clear Screen” feature.
4. Adding / removing symbols from “problematic” locations.
Making the maximum number of changes between frames.
Timing Scenarios - Different timings relatively to the VSYNC signal:
Adding / removing symbols right after / right before a VSYNC arrival.
Adding / removing symbols long after/before a VSYNC arrival.
3. Adding / removing symbols right when VSYNC active pulse arrives.
Notes: רשימת הבדיקות שנעשו בסימולציות ובמעבדה

## Slide 20: Testing: Step by Step…
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
Display Controller
SG Top
VESA ctrl
DC FIFO
VSYNC , req_ln_trig
Opcode Parser
SDRAM model
SG register
WBS
SG WBM IF
WBM
Notes: את תהליך הבדיקתיות ביצענו לאט ובזהירות. בנינו מודלים שונים לחלקים השונים של הפלטפורמה, ואחד אחד הורדנו אותם תוך ביצוע בדיקות:
התחלנו מהורדת ה opcode parser שסיפק את ה opcodes, ובמקומו הכנסנו רגיסטר שיקבל את הפקודות מ WBS.
לאחריו הורדנו את ה SDRAM model וחיברנו את WBM SG IF כדי לבצע גישות אל הזיכרון החיצוני דרך ה Memory manager

## Slide 21: Waveforms Examples
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
Notes: התבוננו ב waveforms השונים. להלן שתי דוגמאות:
איתחול: איפוס ה RAM הפנימי ב SG באפסים + טעינת ה SDRAM החיצוני בסמלים.
שליחת השינויים בין הפריימים אל ה SG + עידכון ה RAM הפנימי בשינויים אלו.

## Slide 22: Simulation GUI
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
Notes: השתמשנו בGUI שבנינו בפעם הקודמת. להלן תזכורת קצרה – לעבור על הכל במהירות...
עשינו diff בין הקבצים המתקבלים לבין אלו המצופים.

## Slide 23: Golden Model
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
Automation
Random Tests
Notes: לאחר תהליך הבדיקתיות ב GUI, שיכללנו את תהליך הבדיקות כך שיתבצע באופן אוטומטי.
בלחיצת כפתור ניתן לקבל tests רנדומליים שונים, ונבנות בצורה אוטומטית תיקיות המכילות את התוצאות השונות.
הדבר סייע בבחינת הסביבה שלנו ותרם לאיתור באגים שונים.

## Slide 24: Final GUI
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
Read from / Write to registers
Notes: לאחר שכל תוצאות הבדיקות עברו בהצלחה, שיפצנו את ה GUI לתוצרתו הסופית:
טעינת הסמלים שבהם נשתמש לSDRAM
מיקומם על גבי המסך ושליחת פקודות UART מתאימות.
הוספת יכולות חדשות של קריאה / כתיבה מרגיסטרים במערכת

## Slide 25: Lab Examination
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
Notes: להלן תיאור של המערכת הכוללת עם חיבור הכרטיס ומסך התצוגה

## Slide 26: DE2 Board – Blinking Led
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
Notes: השתמשנו בלד מהבהב כחלק מבדיקתיות המערכת. הבהובו ב 1Hz מציין כי ה Pll ננעל.

## Slide 27
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
DE2 Board – Registers Values
Notes: את ערכי הרגיסטרים החשובים שבמערכת ייצגנו ע"י תצוגת 7 – segments
הוספנו רגיסטר נוסף (register version ) כחלק מ"סימן חיים" נוסף

## Slide 28: Synthesis Results
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
Notes: צרבנו את המערכת על גבי הכרטיס.
להלן תוצאות quartus המתקבלות:
שימוש ב 13% מסך תכולת ה FPGA

## Slide 29: Problems & Solutions - Example
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
Interfacing Memory Management from Display Controller.
Problem: Platfom does not support this.
Solution: Changing Mem Ctrl RD functionality
Mem Ctrl Rd
SDRAM Arbiter
Mem Ctrl Wr
Memory Management
Display Controller
Symbol Generator
Reg Addr
WRITE
Notes: דברים שלמדנו בפרוייקט

## Slide 30: What have we learned?
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
Planning and Specifying a Project
Integration to an existing platform
Protocols: UART, Wishbone, VESA
Verify logic correctness using waveforms, text files, BMP files and scripts
Synthesis & Place and Route
Integration with real HW
Testing our HW using GUI
Documentation, SVN, Code Review
Notes: דברים שלמדנו בפרוייקט

## Slide 31: Schedule
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
To do… | Due Date
Wishbone integration | 28.11.12
Integration with FPGA | 12.12.12
Synthesis , P&R | 26.12.12
Lab Checks | 2.1.13
Extend GUI capabilities | 9.1.13
Full system simulation and debug | 23.1.13
Final debug in lab | 6.2.13
Final Presentation part B | 20.2.13
Late of 2 months
Notes: עיקוב של חודשיים לעומת תכנון מקורי (חלקים מסויימים לקחו יותר זמן מהמשוער + לחץ מקורסים אחרים)

## Slide 32: Questions ?
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
Notes: שאלות ?

## Slide 33: What next …
Introduction
Top Architecture
Integration
Data Flow
Testability
GUI
Synthesis P&R
Summary
Notes: אולגה: טיול בהודו + סין
יואב: טיול בדרום אמריקה